## Slide 1: Motion Profiling for first tech challenge teams
By Joshua Heinrich | FTC Team 9889

## Slide 2: Why use motion profiling?
Repeatability and Redundancy
  If encoders die, motion profiling will allow the robot to still be accurate
For Points in Autonomous
  Reaches the target/setpoint faster then other methods
Allow Driver to concentrate on other things
  Synchronized motions (multi-axis arm, elevator)

## Slide 3: Methods
Dead Reckoning
PID
Motion Profile

## Slide 4: Dead reckoning
Turn motor on for X seconds
Slower speed is better
Simple
Works if accuracy and precision are not an issue.
Forward(1.0, 1.0);
sleep(400);
Forward(0.0, 0.0);

## Slide 5: Bang-bang control
Same as Dead Reckoning except with feedback
Drive if error > zero
Again, accuracy and precision are weak
while (true) {
error = setpoint – wanted;
if (error > 0)
Forward(1.0);
else if (error < 0)
Reverse(1.0);
else
Stop();
}

## Slide 6: Pid control
Most common control algorithm
Based on Error (Target - Position)
Output change is determined by time, error, and tuning constants

## Slide 7: Feedforword/feedback
Feedforward is where you plan to be
Feedback is correction of the error from where you are to where you should be
Feedback requires sensors to determine position

## Slide 8: Motion profiles
Start at zero velocity
Accelerate to a maximum
Travel required distance
Accelerate to a stop

## Slide 9: Trapezoidal velocity profile

## Slide 10: Generating a motion profile
Many different methods, we will cover continuous
  A continuous Motion Profile is a continuous function. Think of a sin wave
  Discrete Motion Profile
We will be following these equations
  desmos.com/calculator/jjzbgscrcn

## Slide 11: Generating a motion profile
Calculate how long the total profile will take
Calculate how long the acceleration portion will take
Calculate how long the cruising portion will take

## Slide 12: Generating a motion profile
if(t<= accTime)
Position = (0.5 * max_a) + (t * t)
Velocity = max_a * t
Acceleration = max_a
else if(t<=cruiseTime)
Position = (max_v * t) – ((max_v * max_v) / (2 * max_a))
Velocity = max_v
Acceleration = 0
else if(t<totalTime)
Position = (totalTime * max_v) +
(totalTime * max_a * t) –
(max_v * max_v/max_a) –
(0.5 * ((max_a * t * t) + (max_a * totalTime * totalTime)))
Velocity = (max_a * totalTime) – (max_a * t)
Acceleration = -max_a

## Slide 13: Following a motion profile
Proportional Derivative Velocity Acceleration (PDVA) controller
  Note: A PVA controller will be good enough for most applications

## Slide 14: Following a motion profile
The kV and kA do 90% of the control of the motors. kP and kD are used to account for differences in voltage, friction, and uncontrollable factors.