## Slide 1: Motion Profiling for first tech challenge teams
By Joshua Heinrich, Mentor
Cruise Control #9889
September 25, 2020

## Slide 2: Why use motion profiling?

## Slide 3: Why use motion profiling?

## Slide 4: Why use motion profiling?
Repeatability and Redundancy
  If encoders die, motion profiling will allow the robot to still be accurate
  Less overshoot than other algorithms
For Points in Autonomous
  Reaches the target/setpoint faster then other methods
Allow Driver to concentrate on other things
  Synchronized motions (multi-axis arm, elevator)

## Slide 5: Motion profiles
Start at zero velocity, Accelerate to a maximum velocity
Travel at constant velocity for most of the distance
Decelerate to a stop

## Slide 6: Generating a motion profile
Many different methods, we will cover continuous
  A continuous motion profile calculates position, velocity, etc. for every possible time.
  A discrete motion profile only calculates position, velocity, etc. for certain times.
We will be following these equations
  https://www.desmos.com/calculator/ogjgtrgfka

## Slide 7: Generating a motion profile
Calculate how long the total profile will take
Calculate how long the acceleration portion will take
Calculate how long the cruising portion will take

## Slide 8: Generating a motion profile
if(t<= accTime)
Position = (0.5 * max_a) + (t * t)
Velocity = max_a * t
Acceleration = max_a
else if(t<=cruiseTime)
Position = (max_v * t) – ((max_v * max_v) / (2 * max_a))
Velocity = max_v
Acceleration = 0
else if(t<totalTime)
Position = (totalTime * max_v) + (totalTime * max_a * t) –
(max_v * max_v/max_a) – (
0.5 * ((max_a * t * t) + (max_a * totalTime * totalTime)))
Velocity = (max_a * totalTime) – (max_a * t)
Acceleration = -max_a

## Slide 9: Following a motion profile
Proportional Derivative Velocity Acceleration (PDVA) controller
  Note: A PVA controller will be good enough for most applications

## Slide 10: Following a motion profile
The kV and kA do 90% of the control of the motors. kP and kD are used to account for differences in voltage, friction, and uncontrollable factors. These are tuned values.

## Slide 11: Motion profiling in road runner
Road Runner
  Developed by FTC Team 8367, Road Runner is a Kotlin library designed to path planning and following.
  Has many built-in generators and followers
  Does all the math for us!
  Jerk Limited Profile! Can control how quickly the robot accelerates